## Slide 1: Anti-Icing Strategy
ANTI-ICING is a concept in which a chemical, either in a liquid or pre-wetted solid form, is spread directly onto the pavement before snow or ice begins to stick to the surface of the road or during the storm immediately after plowing. This action prevents snow or ice from bonding to the pavement and, thus, prevents a hard-to-remove ice or snow pack from forming during the storm.

## Slide 2: De-icing
De-icing is simply removing snow and ice that has bonded to the road surface
De-icing is more difficult
  Quantities depend on Conditions
  Temperature dependent
  Moisture dependent
    Product May dilute and Refreeze
    Additional Storage May be Needed
    And if goal is to maintain wet roads regardless, Cost will be a Factor