## Slide 1: Did you do a Pre-trip?
Notes: This truck was believed to have a small hydraulic leak in the engine compartment and was out of service for nearly one year before being rebuilt from this fire.

## Slide 2: Vehicle Inspections

## Slide 3: Equipment
Pre-Trip/Post-Trip
  1st Step to Safety
Communicate Problems
  Let others know what is wrong and fill out the work order or notification
Check your Equipment often
  You never know what you might find
Know the areas on the equipment that are constantly under stress

## Slide 4: Preventive Maintenance
Starts with Pre Trip Inspection
  Inspections are used to protect CDOT investments
      Review previous day post trip
    Check all fluids under hood at the beginning of each shift and more often if needed
    Check Tires Air Pressure Weekly with a Gauge
    Check all fluids Monthly
      Differentials
      Transmission / Transfer Case
      Hydraulic System
    Grease equipment Monthly

## Slide 5: Preventive Maintenance
Post Trip Inspection
  Is Required by Federal DOT
    49 CFR Part 396.11 Driver vehicle inspection report. Must be in writing.
  Taught at CDOT Training Academy
  Is Required on CDL exam, must demonstrate that you know what to inspect on Post trip to pass exam.

## Slide 6: Preventive Maintenance Post Trip Requirements
  Service Brakes
  Park Brake
  Steering Mechanism
  Lighting devices and reflectors
  Tires
  Horn
  Windshield wipers
  Rear Vision mirror
  Coupling devices
  Wheels and rims
  Emergency equipment

## Slide 7: Preventive Maintenance

## Slide 8
Notes: Only check the box if there is a deficiency.
Never operate a piece of equipment that has an out of service criteria defect.

## Slide 10: Preventive Maintenance
PRE/POST Trip Inspections.
  Federal DOT is not concerned if there are any fluids in the engine, transmission, differential or transfer case, or if there are any fluids in the steering system or cooling system.
  Their only concern is if they leak and if the unit is safe to operate.
  CDOT DOES, we want to protect our investment. Make sure you check all fluids and they are in operating range.

## Slide 11: Equipment
Attachments (These vary from unit to unit)
  Plows, Wings, Blowers, Sanders, Spray Units
Calibration
  You need to know how much product you are putting out
Preventative Maintenance
  Makes all the Difference
Know the limitations and characteristics of your equipment

## Slide 12: Attachments
Inspection, service, maintenance and use
Calibration
Plow blade inspection and safely changing them

## Slide 13: Cleaning of Equipment
Proper cleaning in an approved area
Inspection of equipment and attachments
Monitor condition of patrol during cleaning
Perform during normal work hours
Notes: Clean, clean, clean. A clean vehicle reduces the corrosion on our fleet. You should never park a vehicle after a storm without washing it off first. The corrosion of any chloride is intensified with the chemical reaction that takes place when the product is allowed to dry and then become wet again. Give example.