## Slide 1: Pavement Temperatures v.s. Air Temperatures
-10
-5
0
5
10
15
20
25
30
35
40
12
2
4
6
8
10
12
14
16
18
20
22
Time of Day
Temperature
Pavement Temperature
Air Temperature
Notes: Before RWIS, the only thing to rely upon was air temperature. Can you see how that may have been deceiving and resulted in less than ideal treatment decisions?

## Slide 2: Influences on Pavement Temperatures
Subsurface Temperature
Air Temperature
Sunlight
Night Sky (clouds put a “lid” on loss of heat to night sky; clear night sky allows more rapid heat loss)
Precipitation
Makeup and color of the road surface - asphalt absorbs more solar heat than concrete

## Slide 3
Influence of Sun on Pavement Temperatures
7:00 a.m.
10:00 a.m.
1:00 p.m.
3:00 p.m.

## Slide 4: Subsurface Temperatures
Due to the density and mass of the earth, subsurface temperatures rise or fall very slowly

## Slide 5: Fall Scenario
Precipitation does not freeze on the pavement, even though air temperature is below freezing

## Slide 6: Winter Scenario
Precipitation will freeze on the pavement, unless treated with deicing chemicals

## Slide 7: Spring Scenario
Precipitation will freeze on the pavement, even though air temperature is above freezing

## Slide 8: Pavement Vs. Deck Temperatures
Bridge decks are not influenced by the subsurface materials
Pavement surface and pavement color of a bridge may differ from surrounding roadways
Structural components of the bridge may retain or release heat differently
Notes: Make connection that this is why bridges receive special attention and may be treated differently – potential for more severe conditions on bridges without a proactive response.

## Slide 9: Pavement Vs. Deck Temperatures
Bridges tend to heat/cool faster than roads
Because there is not subsurface heat to help maintain temperatures….Bridge temperatures typically more closely track air temperatures than the surrounding pavement