## Slide 1: Bridge Frost
When the dew point is greater than the surface temperature and the surface temperature is below freezing, frost begins to form
Frost will form more quickly if the difference between dew point and surface temperature is large

## Slide 2
Example of a Bridge Frost Condition
20
22
24
26
28
30
32
Time
Temperature
Bridge Deck
Dew Point
Bridge
Frost
may
form
1:00 3:00 5:00 7:00 9:00 11:00 1:00
Frost can form!
Notes: Emphasize that dew point and bridge deck temp are what determines if frost will occur.

## Slide 3: Other factors that influence bridge frost
Amount of chemical residue on the surface
Traffic volume- high traffic volume changes frost formation
Wind speed- frost less likely to form when windy
Clear skies - frost more likely to form in clear sky conditions than on a cloudy night
Warm or Cold fronts can drastically change humidity and frost formation

## Slide 4: Bridge Frost Treatment Options
Treat with liquid deicers prior to the anticipated frost event
Apply liquid deicing chemicals on Fridays to help prevent frost from forming over the weekend- must retreat if frost or other precipitation occurs after application
Treat with liquid or pre-wet materials between 5:30-7:00 a.m. the morning of the predicted frost
Treatment option a local decision