## Slide 1: LESSON THREE: Weather Basics

## Slide 2: Weather Basics
Understanding the Weather
Weather Concepts
Pavement Temperature and Dew Point
Precipitation Types
Weather Road Hazards
Storm Conditions

## Slide 3: Understanding the Weather
  Basic Forecasting Issues
  Forecasting Tools
  Pavement Temperature

## Slide 4: Weather Concepts
  Winter Event Categories
  States of Water

## Slide 5: Pavement Temperature and Dew Point
Pavement Temperature
Determines treatment type and duration
Affected by numerous variables
  Air Temperature Trends
  Subsurface Temperatures
  Time of Day
  Cloud Cover
  Wind Speed

## Slide 6: Exercise: Pavement Temperature
During what season does the subsurface hold the most heat? Fall, Winter or Spring?

## Slide 7: Exercise: Pavement Temperature
During what season does the subsurface hold the most heat? Fall, Winter or Spring?
Fall – the ground retains heat from the Summer season

## Slide 8: Pavement Temperature and Dew Point
Dew Point
Measure of moisture in the air
How does this effect the pavement?

## Slide 9: Exercise: Effects of Pavement Temperature and Dew Point
What condition is likely to occur when the dew point is at or above 32ºF and the pavement surface is at or below 32ºF ?

## Slide 10: Exercise: Effects of Pavement Temperature and Dew Point
What condition is likely to occur when the dew point is at or above 32ºF and the pavement surface is at or below 32ºF ?
Frost or black ice

## Slide 11: Precipitation Types
  Rain
  Freezing Rain
  Sleet
  Snow
  A STORM CAN CONTAIN A VARITEY OF PRECIPITATION TYPES!

## Slide 12: Winter Weather Road Hazards
  Frost
  Black Ice
  Freezing Fog
  Blowing Snow
  Storm Runoff
  Compacted Snow
  Slush

## Slide 13: Exercise: Winter Weather Road Hazards
True or False? All winter weather road hazards require the occurrence of rain or snow.

## Slide 14: Exercise: Winter Weather Road Hazards
True or False? All winter weather road hazards require the occurrence of rain or snow.
There are numerous non-precipitation type of winter road hazards (frost, black ice, blowing snow)

## Slide 15: Storm Conditions
 | Temperature | Precipitation | Road Surface
Condition 1 | Near 30º F | Snow, sleet, or freezing rain | Wet
Condition 2 | Below 30º F | Snow, sleet, or freezing rain | Wet or sticky
Condition 3 | Below 20º F and falling | Dry snow | Dry
Condition 4 | Below 20º F | Snow, sleet, or freezing rain | Wet
Condition 5 | Below 10º F | Snow or freezing rain | Accumulation of packed snow or ice

## Slide 16: Weather Forecasting

## Slide 17: Exercise: Lesson Three Review
True or False? Knowledge of basic weather science will help the operator to understand the changes that occur during snow and ice removal operations.

## Slide 18: Exercise: Lesson Three Review
True or False? Knowledge of basic weather science will help the operator to understand the changes that occur during snow and ice removal operations.

## Slide 19: Exercise: Lesson Three Review
_________ forecasts are used to make decisions for actual treatment in snow and ice control.

## Slide 20: Exercise: Lesson Three Review
Short term forecasts are used to make decisions for actual treatment in snow and ice control.

## Slide 21: Exercise: Lesson Three Review
True or False? Most types of winter hazards encountered are forms of water.

## Slide 22: Exercise: Lesson Three Review
True or False? Most types of winter hazards encountered are forms of water.
Water has 3 forms – gas, liquid and solid.

## Slide 23: Exercise: Lesson Three Review
The two most critical weather and environmental factors considered in snow and ice control are _________________ and ________.

## Slide 24: Exercise: Lesson Three Review
The two most critical weather and environmental factors considered in snow and ice control are pavement temperature and dew point.

## Slide 25: Exercise: Lesson Three Review
True or False? Several factors affect pavement temperature.

## Slide 26: Exercise: Lesson Three Review
True or False? Several factors affect pavement temperature.
Air temperature trends, subsurface temperatures, time of day, cloud cover and wind

## Slide 27: Exercise: Lesson Three Review
_________ is a measure of the moisture in the air.

## Slide 28: Exercise: Lesson Three Review
Dew point is a measure of the moisture in the air.
The higher the dew point the greater the moisture in the air. The lower the dew point, the drier the air.

## Slide 29: Exercise: Lesson Three Review
True or False? Frost is less likely to occur when it is windy.

## Slide 30: Exercise: Lesson Three Review
True or False? Frost is less likely to occur when it is windy.
Wind reduces surface moisture and brings warm air down to the surface.

## Slide 31: Exercise: Lesson Three Review
True or False? A storm can contain a variety of precipitation types.

## Slide 32: Exercise: Lesson Three Review
True or False? A storm can contain a variety of precipitation types.
Precipitation types will change as the moisture content of the air and clouds change.

## Slide 33: QUESTIONS ?? LESSON THREE: Weather Basics