## Slide 1: Anti-Icing
Anti-icing vs. Deicing
“Proactive vs Reactive”
Chemicals
  Prewetted salt
  Liquids
Another ‘tool’ for winter operations
  Can reduce, but will not eliminate, need for additional salting or plowing
Notes: Remember, anti-icing is the proactive operation compared to deicing as a reactive operation.
Anti-icing is a strategy generally used to support higher level of service goals.
Why Liquids? - Liquids will give us the ability to place the chemical in the needed area to stop the bonding of ice and snow with less loss of material from bounce and scatter or from traffic.
With anti-icing, we are initially putting material down on a dry road surface prior to the predicted storm. Liquid chemicals (salt brine and other chlorides) are the preferred anti-icing materials and are sprayed onto the road surface using truck-mounted equipment.
Solid ice control chemicals can be effective in anti–icing if they are used properly. Dry solid chemicals cannot be applied before a snow or ice event unless there is a reasonable chance they will stay on the surface. Vehicular traffic and wind can blow dry solid chemicals off paved surfaces. Wetting dry solid chemicals with other liquid chemical solutions before they hit the paved surface makes them stick better and reduces “bounce and scatter” tendencies. Finer gradations of solid chemicals when heavily wet with a liquid will stand up to traffic and wind fairly well.
Liquid ice control chemicals are very useful in an anti–icing program. Liquids can be applied to any paved surface prior to a snow or ice event and remain effective until it reaches critical dilution (the point where the solution will freeze). Liquids are not seriously displaced by traffic and the residue will remain effective for hours or even days in some conditions.
Anti-icing is another ‘tool’ in your winter operations practices.
It is not meant to replace plowing or salt deicing.
It will help to decrease the efforts in plowing and salting that are needed after the storm arrives.

## Slide 2: Anti-Icing Decision Tree

## Slide 3: Anti-Icing Advantages
Applied during better conditions (before the storm)
Snow & ice removed more easily and more quickly
Safety increased in shorter time
Can reduce chemical use by 50 to 80%
Notes: There are several advantages to anti-icing.
  First, we’re applying the chemical during good conditions instead of adverse weather conditions and unsafe roads. And careful management may reduce the need for overtime.
  The snow and ice that accumulates cannot bond to the pavement and can therefore be removed more easily and in a shorter time.
  The shorter time equates to increased safety on the roads.
  The anti-icing chemicals will result in a substantial reduction in subsequent chemical use during the storm, the amount of reduction depending on all the variable conditions of the road, traffic and storm.
  Frost problems can be reduced or eliminated with anti-icing. Since frost is difficult to forecast, the preventive nature of anti-icing has proven to be effective in areas prone to frost or black ice conditions.

## Slide 4: Blizzard Like Conditions
Intense snow, wind, cold
  May want to plow only – consider dilution potential
  Add deicer as temperature warms & blizzard conditions subside
White-out conditions
Stay off road until visibility is restored
Consult with your supervisor
Notes: The worst cases usually occur when the chemical treatment is quickly overwhelmed (diluted) by excessive amounts of water or ice – dilution of solution.
Blizzard conditions (intense snowfall, wind, very cold temperatures) quickly dilute ice control chemicals and can render them virtually useless.
If the pavement temperature going into and coming out of a blizzard is expected to be extremely low, then plowing only may be the best strategy.
After the blizzard, if it is still very cold, you may want to use abrasives as necessary until warmer temperatures will allow chemical deicing to work.
If the pavement temperature throughout and after the blizzard is likely to be fairly warm, a treatment with an ice control chemical before or early in the storm followed by plowing only throughout the storm, will make deicing at the end of the storm much quicker.
Good weather forecasting data and experience will dictate good judgment calls when needed in these conditions.
In situations where falling and/or blowing snow make visibility near zero, it is a good idea to get snow and ice control vehicles well off the road. Operating in those conditions is a risk to everyone involved.

## Slide 5: Freezing Rain
Discuss Scenarios
  Forecast = 2” snow from 5AM to 8AM then changing to freezing rain
  Do you plow off snow or leave on?
Apply solids
  salt and abrasives
  Pre-wetted salt and abrasives
Abrasives give immediate traction
Notes: Rapidly accumulating freezing rain is another maintenance nightmare. The best strategy is to apply solid ice control chemicals, in very narrow bands in the high-side wheel path of each lane.
With luck, there will be a location in each lane that will provide enough friction to allow vehicles to stop and steer.
Freezing rain may dictate the immediate use of a salt/abrasive mix. The abrasives will give immediate traction while the salt will start the melting action needed to control icy conditions. (Heavy freezing rain may quickly smother abrasives and chemicals if applied in wider bands.)