## Slide 1: Blizzard Like Conditions
Intense snow, wind, cold
  May want to plow only – consider dilution potential
  Add deicer as temperature warms & blizzard conditions subside
White-out conditions
Stay off road until visibility is restored
Consult with your supervisor
Notes: The worst cases usually occur when the chemical treatment is quickly overwhelmed (diluted) by excessive amounts of water or ice – dilution of solution.
Blizzard conditions (intense snowfall, wind, very cold temperatures) quickly dilute ice control chemicals and can render them virtually useless.
If the pavement temperature going into and coming out of a blizzard is expected to be extremely low, then plowing only may be the best strategy.
After the blizzard, if it is still very cold, you may want to use abrasives as necessary until warmer temperatures will allow chemical deicing to work.
If the pavement temperature throughout and after the blizzard is likely to be fairly warm, a treatment with an ice control chemical before or early in the storm followed by plowing only throughout the storm, will make deicing at the end of the storm much quicker.
Good weather forecasting data and experience will dictate good judgment calls when needed in these conditions.
In situations where falling and/or blowing snow make visibility near zero, it is a good idea to get snow and ice control vehicles well off the road. Operating in those conditions is a risk to everyone involved.

## Slide 2: Freezing Rain
Discuss Scenarios
  Forecast = 2” snow from 5AM to 8AM then changing to freezing rain
  Do you plow off snow or leave on?
Apply solids
  salt and abrasives
  Pre-wetted salt and abrasives
Abrasives give immediate traction
Notes: Rapidly accumulating freezing rain is another maintenance nightmare. The best strategy is to apply solid ice control chemicals, in very narrow bands in the high-side wheel path of each lane.
With luck, there will be a location in each lane that will provide enough friction to allow vehicles to stop and steer.
Freezing rain may dictate the immediate use of a salt/abrasive mix. The abrasives will give immediate traction while the salt will start the melting action needed to control icy conditions. (Heavy freezing rain may quickly smother abrasives and chemicals if applied in wider bands.)