## Slide 1: Chemicals: How do they work?
Depress the freezing point of water, turning ice or snow into liquid or slush
Solid salts dissolve to form brine solution
Notes: Generally, all deicers work in the same way. They depress the freezing point of water and turn snow and ice into a liquid or a semi-liquid slush. Solid chemical salts bore through ice and snow, dissolving to form a strong brine solution which spreads under the ice or hard-packed snow, undercutting and breaking the bond to the road surface. Once the bond is broken, the ice and snow can be plowed off or removed by other means. By applying material prior to the storm, we can prevent the bond to the road surface and melt the snow and ice as it comes in contact with the brine.
Agricultural byproducts work much the same way but do not form a brine. They are soluble in water and the resulting solution acts by depressing the freezing point of snow and ice. As stated before, these products are usually used in combination with other materials.
Although all these materials work in the same way, they vary widely in performance. By performance, we have to consider several factors – effective temperature range, speed, amount of material required, and duration of melting action.

## Slide 2: Chemical Terms
Concentration
  % by weight of chemical in solution
Eutectic Temperature
  Lowest Temp solution will melt ice
Endothermic
  Requires heat when going into solution
Exothermic
  Gives off heat when going into solution
Hygroscopic
  Draws water from the air
Notes: To talk about performance, we should first discuss some chemical terminology.
  Concentration
  Eutectic Temperature
  Endothermic
  Exothermic
  Hygroscopic

## Slide 3: Dilution of Solution
Explains why one application rate will not fit all winter events
Application effectiveness will depend on:
  Road surface temperature
  Application rate
  Concentration
  Moisture
Notes: As you can see, we really need to understand this ‘dilution of solution’.
Dilution of solution explains why one application rate will not fit all winter events.
Temperature, moisture, intensity of each event (amount of snow, duration, rate of snowfall) can vary considerably and therefore vary the effectiveness of your chemical application.

## Slide 4
Salt in it’s solid form need’s to turn into a solution/brine before the melting process can occur
When you apply a deicer and before it can begin the process of melting, it must absorb heat from it’s surroundings, air or pavement this process is called endothermic
So how does that relate to rock salt on the
road?
Materials: Salt 101
Notes: 4

## Slide 5
When you apply rock salt the heat required for the melting action must come from somewhere, the air, brine solution (pre-wetting) , the roadway or the subsurface
In October of 2007, a strike-off letter was sent out to the Districts is to make all Department trucks pre-wet capable by November 2010. Counties are also to establish pre-wet storage tanks at all stockpiles (tank farms) before 2010
Salt/Sodium Chloride

## Slide 6
Eutectic Temperature (freeze point of a chemical): -6 Degrees
Effective Temperature: 15 Degrees
Hygroscopic: A chemical is said to be hygroscopic when it has a tendency to attract moisture; however, with rock salt, the humidity has to be much higher before it can begin absorbing moisture from the air. The relative humidity has to exceed 75% before salt will begin to attract moisture.
Sodium Chloride
Specifications

## Slide 7
Effectiveness drops with temperature
Salt
Notes: Salt also has some disadvantages:
One of the disadvantages is that salt starts to lose its effectiveness when temperatures drop below 20 degrees F.
The lower the temperature, the more salt is needed and a longer time for it to take effect.
Salt is also corrosive as are all the chlorides. Proper vehicle washing is essential when using salt to minimize this corrosiveness.
And then there are the environmental concerns, impacts on water quality, soil fertility and plants. Most all the environmental problems can be contributed to two causes - excessive use of salt on the roadway and improper storage.
If salt is used effectively and stored properly, you should not have environmental problems.
We’ll talk about salt storage and containment facilities later.

## Slide 8: Other Natural Salts
Calcium Chloride
  Exothermic: gives off heat
  Hygroscopic: attracts moisture
  Eutectic Temp: -60oF
  30-33% concentration in solution
Magnesium Chloride
  Exothermic: gives off heat
  Hygroscopic: attracts moisture
  Eutectic Temp: -28oF
  22-26% concentration in solution
Notes: Both of these materials are exothermic, giving off heat when they go from solid into solution. Both are hygroscopic, attracting moisture from the air or the surroundings, improving their effectiveness in dry cold conditions.
Both have low eutectic temperatures meaning we get more melting action at lower temperatures. This factor makes them advantageous as prewetting materials for salt, particularly when the temperatures drop below 20oF
Calcium chloride is usually sold in a 30-33% solution and magnesium chloride at a 23-26% solution. These concentrations relate back to the respective eutectic temperatures of these materials.