## Slide 1: Spreading Operations
Policies and Procedures
Mix ratios/rates
Notes: In this section we need to discuss:
  Policies and procedures regarding plow operation
  Actual plowing techniques for different types of roads and for different situations. We’ll also look at the use of different types of plows.
  And we’ll consider those special problems that may be encountered while plowing.

## Slide 2
First Priority Routes – Pre-Wet Salt
In order for a chemical to act as a freezing point depressant,
the chemical must go into a solution. The rate at which salt
goes into a solution can be accelerated if a liquid is added.
The type of liquid and methods used to pre-wet salt varies
depending on the resources. Suggested application rates for
the liquid vary from 6 to 12 gallons per ton of salt. Salt that
contains a lot of fine material or has a higher moisture
content will require less liquid to be added.
4.5.3 MATERIAL APPLICATIONS AND PLOWING PROCEDURES FOR FIRST, SECOND AND THIRD PRIORITY ROUTES
Spreading Operations
Notes: 4.5.3 MATERIAL APPLICATIONS AND PLOWING PROCEDURES FOR FIRST, SECOND AND THIRD PRIORITY ROUTES
First Priority Routes
PRE-WETTING SALT
In order for a chemical to act as a freezing point depressant, the chemical must go into a solution. The rate at which salt goes into a solution can be accelerated if a liquid is added. The type of liquid and methods used to pre-wet salt varies depending on the resources. Suggested application rates for the liquid vary from 6 to 12 gallons per ton of salt. Salt that contains a lot of fine material or has a higher moisture content will require less liquid to be added. To achieve the most benefit from adding a pre-wetting agent to dry salt is after pavement temperatures should be no more than 24 degrees and is falling. Pre-wetting salt at a temperature above 25 degrees could have a minimal impact on increased efficiency.

## Slide 3
These roads may be treated with straight salt or salt
mixed with a chemical enhancer.
A salt/anti-skid mix can be used when conditions
are such that straight chemical applications are not
effective due to lower temperatures.
Although the decision to use a straight chemical
application or a salt/anti-skid mix is basically a field
decision, the following slide shows application rate guidelines
Which are suggested for first priority highways:
First Priority Routes - Spreading Operation
Spreading Operations
Notes: 4.5.3 MATERIAL APPLICATIONS AND PLOWING PROCEDURES FOR FIRST, SECOND AND THIRD PRIORITY ROUTES (Continued)
First Priority Routes
SPREADING OPERATION
These roads may be treated with straight salt or salt mixed with a chemical enhancer. A salt/anti-skid mix can be used when conditions are such that straight chemical applications are not effective due to lower temperatures. Although the decision to use a straight chemical application or a salt/anti-skid mix is basically a field decision, the following application rate guidelines are suggested for first priority highways:
If Surface Temperature Application Rate of
Is: Dry or Pre-wetted Salt:
25°F or above: 130 lbs. of dry or pre-wet
salt per Snow Lane Mile.
20°F to 25°F 170 lbs of pre-wet salt
per Snow Lane Mile.
10°F to 20°F 230 lbs. of pre-wet salt
per Snow Lane Mile.
Below 10°F Recommend Straight
Anytime Anti-Skid be used*
*It is permissible to add a small amount of salt to anti-
skid to keep the material from freezing.

## Slide 4
First Priority Routes - SPREADING OPERATION
During cold temperatures, the ability of chemicals to react and
the effectiveness of individual or combinations of deicing
materials is difficult to predict.
A straight salt application may be effective with heavy traffic,
sunlight and calm air.
Spreading Operations
Notes: 4.5.3 MATERIAL APPLICATIONS AND PLOWING PROCEDURES FOR FIRST, SECOND AND THIRD PRIORITY ROUTES (Continued)
First Priority Routes
SPREADING OPERATION
During cold temperatures, the ability of chemicals to react and the effectiveness of individual or combinations of deicing materials is difficult to predict. A straight salt application may be effective with heavy traffic, sunlight and calm air. If available, a premixed combination of 5 parts salt to 1 part bag calcium chloride may prove effective or a liquid chemical deicer may be mixed with salt by field personnel. Mixtures of anti-skid material and salt ranging from 1, 2 or 3 parts of salt to 1 part of anti- skid to salt can be used at low temperatures with the mix shifting more heavily to anti-skid material as the temperature drops. Anti-skid salt mixes provide traction until salt reaction takes place. Under certain conditions, the granular nature of salt may provides traction until melting action takes place. Liquid enhancers such as Salt Brine, Calcium Chloride or Magnesium Chloride may be used as a pre-wetting agent to augment the activity of the salt. Rate of usage for liquid chemicals should be as per the manufacturers’ recommendations. Ultimately field personnel must decide the final selection of deicing materials or a combination of materials.

## Slide 5
First Priority Routes
Spreading Operation
If Surface Temperature Application Rate of Is: | Dry or Pre-wetted Salt:
25°F or above: | 130 lbs. of dry or pre-wet salt per Snow Lane Mile.
20°F to 25°F | 170 lbs of pre-wet salt per Snow Lane Mile.
15°F to 20°F | 230 lbs. of pre-wet salt per Snow Lane Mile.
Below 15°F | Recommend Straight Anti-Skid be used*
Spreading Operations
Spreading Operations
Notes: 4.5.3 MATERIAL APPLICATIONS AND PLOWING PROCEDURES FOR FIRST, SECOND AND THIRD PRIORITY ROUTES (Continued)
First Priority Routes
SPREADING OPERATION
These roads may be treated with straight salt or salt mixed with a chemical enhancer. A salt/anti-skid mix can be used when conditions are such that straight chemical applications are not effective due to lower temperatures. Although the decision to use a straight chemical application or a salt/anti-skid mix is basically a field decision, the following application rate guidelines are suggested for first priority highways:
If Surface Temperature Application Rate of
Is: Dry or Pre-wetted Salt:
25°F or above: 130 lbs. of dry or pre-wet
salt per Snow Lane Mile.
20°F to 25°F 170 lbs of pre-wet salt
per Snow Lane Mile.
10°F to 20°F 230 lbs. of pre-wet salt
per Snow Lane Mile.
Below 10°F Recommend Straight
Anytime Anti-Skid be used*
*It is permissible to add a small amount of salt to anti-
skid to keep the material from freezing.

## Slide 6
Secondary priority routes are characterized by median barriers, traffic
separators, drainage facilities, etc., which present cleanup problems when
abrasives are spread.
Abrasives are recommended on second priority routes under the following
conditions:
  Temperature is 20°F and falling during daylight hours.
  Steep grades and curves during non-peak traffic hours to provide traction.
  Plowing operations should be scheduled to give priority to routes heading into major work areas in the morning and outbound routes in the afternoon hours.
Second Priority Routes
Salt may be used on second priority routes to accommodate
high volume of traffic as conditions warrant.
Spreading Operations
Notes: 4.5.3 MATERIAL APPLICATIONS AND PLOWING PROCEDURES FOR FIRST, SECOND AND THIRD PRIORITY ROUTES (Continued)
Second Priority Routes
Salt may be used on second priority routes to accommodate high volume of traffic as conditions warrant.
Secondary priority routes are characterized by median barriers, traffic separators, drainage facilities, etc., which present cleanup problems when abrasives are spread.
Abrasives are recommended on second priority routes under the following conditions:
Temperature is 20°F and falling during daylight hours.
Steep grades and curves during non-peak traffic hours to provide traction.
Plowing operations should be scheduled to give priority to routes heading into major work areas in the morning and outbound routes in the afternoon hours.

## Slide 7
If Surface Temperature Application Rate of Is: | Dry or Pre-wetted Salt:
25°F or above: | 130 lbs. of dry or pre-wet salt per Snow Lane Mile.
20°F to 25°F | 170 lbs of pre-wet salt per Snow Lane Mile.
15°F to 20°F | 230 lbs. of pre-wet salt per Snow Lane Mile.
Below 15°F | Recommend Straight Anti-Skid be used*
Second Priority Routes - Spreading Operation
Spreading Operations
Notes: 4.5.3 MATERIAL APPLICATIONS AND PLOWING PROCEDURES FOR FIRST, SECOND AND THIRD PRIORITY ROUTES (Continued)
Second Priority Routes
The following application rate guidelines are recommended for second priority routes. Deviations from these guidelines may be justified by factors such as weather forecasts, road conditions, material availability and time.
If Surface Temperature Application Rate of
Is: Dry or Pre-wetted Salt:
25°F or above: 130 lbs. of dry or pre-wet
Time: 6 am to 6 pm salt per Snow Lane Mile.
20°F to 25°F 170lbs of pre-wet salt
Time: 6 am to 6 pm per Snow Lane Mile.
10°F to 20°F 230 lbs. of pre-wet salt
Time: 6 am to 6 pm per Snow Lane Mile.
Below 10°F Recommend Straight
Anytime Anti-Skid be used*
*It is permissible to add a small amount of salt to anti-skid to keep the material from freezing.

## Slide 8
Straight salt should not be used on low traffic volume third
priority roads. Treatment for these roads will primarily be a
mixture of 3 parts anti-skid material to 1 part salt or straight
anti-skid. With this type of material being used, weather
conditions and temperatures are the limiting factors.
Third Priority Routes
Since it is not required to completely clear low traffic volume
third priority routes of snow by any action other than
plowing, continuous material applications over the entire
roadway length may not be necessary.
Spreading Operations
Notes: 4.5.3 MATERIAL APPLICATIONS AND PLOWING PROCEDURES FOR FIRST, SECOND AND THIRD PRIORITY ROUTES (Continued)
Third Priority Routes
Since it is not required to completely clear low traffic volume third priority routes of snow by any action other than plowing, continuous material applications over the entire roadway length may not be necessary. Straight salt should not be used on low traffic volume third priority roads. Treatment for these roads will primarily be a mixture of 3 parts anti-skid material to 1 part salt or straight anti-skid. With this type of material being used, weather conditions and temperatures are the limiting factors. It is important to spread the critical areas as soon as noticeable snowfall (1/2" to 1") has accumulated in order to establish a good base of material to provide vehicle traction. Also, since the goal here is to spot spread select locations, heavier material application rates are required. The following application rate guidelines are recommended for third priority roads. Deviation from these guidelines may be justified by factors such as weather forecasts, road conditions, material availability or time.
Temperature - Not a factor
Recommended Material - 3 parts anti-skid to 1 part salt or straight anti-skid.
Recommended Application Rates –

## Slide 9
Third Priority Routes
It is important to spread the critical areas as soon as
noticeable snowfall (1/2" to 1") has accumulated in order to
establish a good base of material to provide vehicle traction.
Also, since the goal here is to spot spread select locations,
heavier material application rates are required.
The following application rate guidelines are recommended
for third priority roads. Deviation from these guidelines may
be justified by factors such as weather forecasts, road
conditions, material availability or time.
Spreading Operations
Notes: 4.5.3 MATERIAL APPLICATIONS AND PLOWING PROCEDURES FOR FIRST, SECOND AND THIRD PRIORITY ROUTES (Continued)
Third Priority Routes
Since it is not required to completely clear low traffic volume third priority routes of snow by any action other than plowing, continuous material applications over the entire roadway length may not be necessary. Straight salt should not be used on low traffic volume third priority roads. Treatment for these roads will primarily be a mixture of 3 parts anti-skid material to 1 part salt or straight anti-skid. With this type of material being used, weather conditions and temperatures are the limiting factors. It is important to spread the critical areas as soon as noticeable snowfall (1/2" to 1") has accumulated in order to establish a good base of material to provide vehicle traction. Also, since the goal here is to spot spread select locations, heavier material application rates are required. The following application rate guidelines are recommended for third priority roads. Deviation from these guidelines may be justified by factors such as weather forecasts, road conditions, material availability or time.
Temperature - Not a factor
Recommended Material - 3 parts anti-skid to 1 part salt or straight anti-skid.
Recommended Application Rates –

## Slide 10
Third Priority Application Rate Guideline |  |  | 
Anti-Skid/Salt Mix (AS) (S) | 75/25 AS/S Mix | 50/50 AS/S Mix | 
Not Temperature Dependent | 270 lbs. | 200 lbs. | 
Surface Temperature Below 10o Recommend Straight Anti-Skid Applications. It is permissible to add a small amount of salt to anti-skid to keep the material from freezing. |  |  | 
Application Rate based on a single Snow Lane Mile application. |  |  | 
Third Priority Routes - Spreading Operation
Spreading Operations

## Slide 11
Spreading materials shall be confined for the most part to hills and curves
and other hazardous areas. It is permissible to exceed the maximum
application rate limitations listed above based on local road conditions.
.
Third Priority Routes
Snow lane mile assignments on these roads, especially the MFC-E
roads, will be too long to allow trucks to spread the entire length of their
route. Therefore, the Department will rely mainly on plowing operations
to maintain these roads.
Spreading Operations
Notes: 4.5.3 MATERIAL APPLICATIONS AND PLOWING PROCEDURES FOR FIRST, SECOND AND THIRD PRIORITY ROUTES (Continued)
Third Priority Routes
Snow lane mile assignments on these roads, especially the MFC-E roads, will be too long to allow trucks to spread the entire length of their route. Therefore, the Department will rely mainly on plowing operations to maintain these roads.
Spreading materials shall be confined for the most part to hills and curves and other hazardous areas. It is permissible to exceed the maximum application rate limitations listed above based on local road conditions.
Any location with long or steep hills or sharp curves where the proposed application rate could constantly exceed the recommended application rate must be pre-approved by the County Maintenance Manager.

## Slide 12: Table 2: Notes
NR = Not Recommended
Specific Notes:
Values for ‘solid’ apply to prewet solid & include equivalent dry chemical weight in prewetting solutions
Liquid values are for a 23% concentration solution
In unbonded, try mechanical removal without chemicals. If pretreating, use this rate
If very thin ice, liquids may be applied at unbonded rates
Notes: We should review the notes associated with Table 2.
Review notes using this slide and the next slide.

## Slide 13: Table 2: Notes
General Notes:
5. These application rates are starting points. Local conditions and experience should be used to refine these guidelines.
6. Prewetting chemicals should allow rates to be reduced up to 20% depending on factors such as spread pattern and speed.
7. Application rates for other chemicals are shown in Table 3.
8. Before applying any chemical, surface should be plowed.
Notes: Review General notes.
You can refer to the handout for Table 3 with a review/explanation and discussion as desired. The application rates for four other chemicals are compared to an equivalent application rate for salt for the respective temperature ranges in Table 2.
We will be discussing prewetting and anti-icing and associated rates later in the session.

## Slide 14
1/3
1/3
1/3
46% in center
12%
15% off road
100% salt spread in center 1/3 of road
Typical Scatter of
Road Salt
Notes: Bounce and scatter tends to waste material.
A typical field research project is demonstrated by this drawing - if 100% of salt is spread in the center 1/3 of a dry road, only 46% stays in the center with 12% on each of the outer thirds of the road, and we can lose 15% off each side of the road.
That equates to a 30% loss of material off the road.

## Slide 15
1/3
1/3
1/3
78% in center
9%
2% off road
100% prewetted salt spread in center 1/3 of road
Typical Scatter of
Pre-wetted Road Salt
Notes: If we spread prewetted salt on the center 1/3 of a dry road, 78% percent remains in the center, with 9% going to each outer third, and 2% off each edge of the road.
Giving a total loss of only 4% of the material spread.
Comparing the 30% loss and the 4% loss indicates that we could apply 26% less prewetted salt on the road and get the same results - actually better results since the prewetted salt will give more effective melting action.